## Slide 1: KEK test beam plan
1) Planed in Dec (asking one week of test beam at KEK-PS pi2 beam line; 1 - 4 GeV/c)
2) Prototype test
  Type-A; 12 x 12 w/ 3” PMT (BELLE)
  Type-B; 20 x 20 w/ 3” PMT
  Type-C; 20 x 20 w mirror
beam
beam
PMT
Aerogel

## Slide 2
3) Items to be tested
  Base ideas (http://utkhii.px.tuskuba.ac.jp/)
    # of p.e. vs. momentum (0.4 - 4GeV/c)
    # of p.e. vs. thickness
    Position of PMT
    Air between Aerogel and PMT
    Direction of stack
  Other examples of ideas (raised from personal discussions with K.Ozawa)
    # of p.e. vs. indices (1.007, 1.015, 1.020)
    Different PMTs (What is the situation of Russian PMT?)
    Different product companies of aerogel
    Effect of reflector (use millpore, black paper, etc.)
    Using PID (e/ by gas Cherenkov, Scintillation light(?) might exist )
  Any other ideas ?