## Slide 1
Aerogel counter Prototype Beam Test
T531 in KEK-PS T1
Summary
Common items.
Beam; +2GeV/c
Aerogel; Matsushita SP-15 (n=1.016)
PMT; HAMAMATSU R6233(3”)
Prototype; Integration Sphere Type
Particle Separation
Light Yield (Number of photoelectrons)
Timing property of ACC (Zolin3)
4. Hit Position information by ACC itself (Zolin3)

## Slide 2
Particle selection by TOF
(2GeV/c, positive)
1. Particle Separation
Cherenkov threshold

## Slide 3
Cross Section [cm x cm] | Aerogel [cm] | Integration [cm] | Npe,F (0,0) | Npe,F (0,6) | Npe,B (0,0) | Npe,B (0,6) | Attenuation Length [cm]
15 x 15 | 12 | 12 | 17 | 16 | 15 | 14 | 67
15 x 15 | 12 | 9 | 18 | 18 | 16 | 15 | 44
15 x 15 | 9 | 9 | 15 | 15 | - | - | 44
15 x 15 | 9 | 6 | 13 | 12 | 11 | 11 | 32
2. Light Yield (Number of photoelectrons)
15 x 15 Type
* Npe,F for Forward direction
Npe,B for Backward direction

## Slide 4
Zolin3 Type
Zolin2 Type
Cross Section [cm x cm] | Aerogel [cm] | Integration [cm] | Npe,F (0,0) | Npe,F (0,8) | Npe,B (0,0) | Npe,B (0,8)
11.5 x 21 | 11 | 11 | 9 | 7 | 8 | 8
11.5 x 21 | 11 | 11 | 9 | 10 | 8 | 7
PMT1
PMT2
Cross Section [cm x cm] | Aerogel [cm] | Integration [cm] | Npe,F (0,0) | Npe,F (0,6) | Npe,B (0,0) | Npe,B (0,6) | Attenuation Length [cm]
22 x 12 | 12 | 9 | 15 | 17 | 14 | 13 | 38
22 x 12 | 8 | 13 | 13 | 13 | 12 | 12 | 28
22 x 12 | 9 | 9 | 13 | 14 | 12 | 12 | 42

## Slide 5
Y
X
Beam
(0,0)
15cm
15cm
PMT1
PMT2
15 x 15 Type

## Slide 6
Y
X
Beam
(0,0)
11.5cm
21cm
PMT1
PMT2
Zolin2 Type

## Slide 7
Y
X
Beam
(0,0)
22cm
12cm
PMT1
PMT2
Zolin3 Type

## Slide 8
3. Timing property of ACC (Zolin3)
Timing Resolution ~ 1 ns
Correlation of TDC and ADC

## Slide 9
TDC distribution (Zolin3, counter edge; X=-12cm)
Red; Pions
Blue; Protons
Cherenkov from Aerogel
Hit on PMT window
From PMT interior
~8 ns (Propagation time of Cherenkov light)

## Slide 10
X=-11.75cm
Hit Side
~450 p.e.
Opposite side
~2 p.e.
Cut in this region
Hit on PMT window

## Slide 11
4. Hit Position information by ACC itself (Zolin3)
Propagation Time
Light Yield
Ratio of Npe
Ratio of Propagation time
(Error bar ; rms of distr.)

## Slide 12
Combination of Npe and P.T.
Time difference of PMT1 and PMT2