## Slide 1: Development of high timing resolution Cherenkov beam counter （高飛行時間分解能チェレンコフ・ビームカウンターの開発）
CONTENTS
1.Introduction
2.Cherenkov beam counter
3.Experimental result
4.Summary
S.Sakai S.Esumi M.Ono A.Kiyomichi Y.Kuroki S.Sato M.Shindou A.Danmura H.Tsuruoka H.Masui Y.Miake
Univ. of Tsukuba
Notes: 1.Introduction
2.Cherenkov beam counter
3.Experimental result
4.Summary

## Slide 2: Introduction
PID
(Particle Identification)
Quality of PID
Timing resolution of TOF (Time Of Flight)
“To improve timing resolution of TOF, it is necessary to improve
timing resolution of the beam and stop counter”
Notes: What’s happen?
PID (Particle Identification)
TOF (Time Of Flight)
Quality of PID
Timing resolution of TOF (Time Of Flight)
σ
To improve timing resolution, it is necessary to improve timing resolution of the beam counter

## Slide 3: Why we chosen Cherenkov light?
Response ~ｐｓ
Response ~nｓ
Cherenkov light
Scintillation light
Heavy ion beam
(NA44,WA98 at CERN SPS)
Directivity
“The emission time of Cherenkov light is much faster than that of scintillation light, the timing resolution is expected to be better by using Cherenkov light. “
Notes: Response・・・～ps
Expected high timing resolution
Directivity
(WA98 at CERN SPS)
Since the emission time of Cherenkov light is much faster than that of scintillation light, we think the timing resolution is expected to be better using Cherenkov radiator.
Scintillation light
Cherenkov light
Problem

## Slide 4: Problem
Minimum ionizing particle beam (z=1)
The number of photons is very small
Timing resolution
Optical system which collects photons efficiently needs !
“Timing resolution is inversely proportional to the number of photons, it is important to have optical system which collects photons efficiently”
Notes: Minimum ionizing particle beam
N is very small
Timing resolution
optical system which collects photons efficientry
Timing resolution is inversely proportional to the number of photons, it is important to have optical system which collects photons efficiently.

## Slide 5: New Optical System
“If the Cherenkov emission direction is parallel to the parabola axis, Cherenkov photons are collected on the focal point”
focal point.
focal point.
beam
Notes: Focal point
reflecting all incoming light parallel to its axis to a
focal point.
“If the Cherenkov emission direction is parallel to the parabola axis, cherenkov photons are collected on the focal pointg”
beam

## Slide 6: Cherenkov beam counter(1)
Hamamatsu H2431
TTS = 370 (ps)
Rise Time = 0.7(ns)
Total reflection region・・・11cm
22cm
beam
Notes: Hamamatsu H2431
TTS = 370 (ps)
Raise Time =
All reflection region
22cm
beam

## Slide 7: Experimental Setup
REF1
REF2
VETO
DEF1
DEF2
DEF3
Cherenkov beam counter
Trigger = VETO × DFF1 × DEF2 × DEF3 × STR1 × STR2
Beam・・・２GeV/c
beam
KEK-T1 Beam Line
(T479)
Notes: Trigger = VETO × DFF1 × DEF2 × DEF3 × STR1 × STR2
MEASURE
Charge distribution
beam
Beam・・・２GeV/c
KEK-T1 Beam Line

## Slide 8: Photon yields Distribution
Counts
[pC]
From Radiator+PMT Window
From PMT Window
222.8 pC
11.5 pC
[pC]
211 pC
470
[pC]
N
The number of photoelectrons=470
Notes: Counts
Number of photons
222.8 pC
11.5 pC
211 pC
470
N

## Slide 9: Optical Monte Carlo Simulation
Experimental Result
Optical Monte Carlo Simulation
“The experimental result was well described by Cherenkov simulation.“
0
5
10
15
Reflectivity at the aluminum foil
Absorption in the aclylite
Quantum efficiency
Index of aclylite
Beam size
Notes: Experimental Result
Monte Carlo Simulation
“The experimental result was well described by Cherenkov simulation.“
Q.E
Transmittance of Aclylite

## Slide 10: Timing Resolution
Sigma=41.7 ps
CHK-REF2
Sigma=36.3 ps
REF2-REF1
Sigma=41.7 ps
CHK-REF1
Sigma=36.6 ps
CHK-REF2
Sigma=36.3 ps
CHK-(REF1+REF2)/2
Sigma=28.6 ps
Notes: Sigma=41.7 ps

## Slide 11: Analysis
“The timing resolution of the Cherenkov beam counter
is about 21 (ps)”
1.
2.
Notes: The timing resolution of the Cherenkov beam counter is about 21 (ps)
1.

## Slide 12
Performance of PMT
Experimental result
Timing-resolution (ps)
The number of photoelectrons
21 ps
470
Notes: The number of photoelectron
21 ps
470

## Slide 13: Summary
・To improve timing resolution of TOF, it is necessary to improve timing resolution of the beam and stop counter.
・We have developed Cherenkov beam counter which is used parabola.
・The timing resolution of the Cherenkov beam counter is about 21 ps.