## Slide 1
Data is sent to PC.
Development of Front-End Electronics
for time projection chamber (TPC)
Introduction
Our purpose is development of front-end electronics for TPC. Printed circuit board (PCB), Control data-taking program and Analysis / visualization program are made . We present our development as follows .
TPC is a 3-D tracking gas detector to determine the position of charged particle. When a charged particle ionizes the gas,electrons are made. The electrons drift to wire chamber along electric filed and avalanche is formed near anode wire. It makes a signal on each pad. From the channel of the pad and the timing of the signal, We reconstruct 3-D trajectory of the charged particle.
What is TPC?
Conclusion
Analytical Program
Control Program
Production of PCB
We designed PCB with following specs: 8 analog input channels (8 ADC’s, 8 Preamplifiers) 1 Field programmable gate array (FPGA) 100 MHz clock generator 32-bit output port 16-bit input port 12-bit I/O port Board size (18.3cm x 22.5 cm) Board material (FR4) 2 layers
A/D Conversion
Program language is Visual Basic .net. We develop this program to readout data from the circuit , plot trajectory in 3D image , reconstruction of wave form, and assign color according to amplitude, etc. They are shown below.
Main screen
Data read
Extract signal intensity ,
sampling number data
Plot and Display
extract #N Pad data
Geometric transformation
N=Pad number
N=72
N+=1
M=sampling number
M=1024
M+=1
Y
Y
N
N
FADC converts the analog signal from TPC to the digital data (10-bit). The data of ten bits sent from FADC is digital signals.
Analog signal from TPC
Convert to Digital signal
0001100110 1011011011
AD conversion data
divides into 1024 pieces
When the start signal comes, FPGA begins to take data till 1024 .When data are transferred to PC, ADC address and data address are added. taking data. Since clock frequency is 100 MHz,data are taken each 10 nano seconds .
Channel Map shows signal tension by color
Wave form shows a change of signal of one input channel
Flight Tracker shows particle trajectory. 2 left screen is plot 2-D . Right screen is plot 3-D. Below figures are method of projection. A red line is a common lone in two figures.
9/21/2005 in HAW05
Inst. of Physics. Univ. of Tsukuba Asuka Saito. Shigeru Kiuchi. Yasuo Miake. Tatsuya Chujo. Shinichi Esumi. Sumio Kato . Takanori Aoki. Kentaro Miki. Yoshihiko Nagata. Tsukuba College of Technology Motoi INABA
n←1
n←n+1
n>1024
Yes
No
Parity bit added
end
The data that came from TPC
is preserved in address(n).
Initialization
Waiting for start-trigger
start
θ
Φ
Y
Y
Z
X
X
Z
Define two coordinates for a trajectory: one is detector coordinate. another is observer coordinates . Transform the trajectory from one to the other coordinate. Project the trajectory in the observer coordinate.
Detector coordinates
Observer coordinates
Data flow from reading data to display
Block Diagram
TPC
FADC x
8
PC
PreAMP x
8
Trigger Counter
FPGA
When Trigger counter sends start signal to FPGA on FEM (front-end module), FPGA starts to collect data from ADC and stocks them inside the memory.
FPGA sends request signal to PC, after data taking of 1024 data. If PC accepts the request signal, data transfer from FPGA to PC starts. ADC address ( input channel number ) and data address ( signal number ) are added. The parity bit is added in order to judge whether data are correct or not.
3-state buffer
Front-end module # 1
Front-end module # 2
Front-end module # 9
Y
X
Z
Particle orbit
Anode Wire
Cathode pad
Electric Field
Drift of Electron
Image of TPC
Simulation of Verilog HDL for Data taking
ADC divides from 0v to 1v into 1024 pieces. If ADC is sent over 1v,ADC send error signal to FPGA.
PC is sent 25-bit per 1 channel . The data of binary notation is converted into the data of decimal notation in PC. The data is recorded in PC as data of 10 digits.
Based on the read-out test with proto-type, we have determined the design and parameters of the front-end circuit board. Production of remaining circuit boards has started. A control and an analysis program as well as 3D visualization programs have been prepared and tested with proto-type circuit. The final verification of the program will be done, when the production is finished. Once all 72 signal channels of TPC are operated, the detector performance (position resolution and efficiency) will be evaluated .
Input run number