## Slide 1: Study of jet trigger with ALICE EMCAL for PbPb 5.5TeV
Masato Sano
University of Tsukuba
Lawrence Berkeley National Laboratory
Research Fellow of the Japan Society for the Promotion of Science
Notes: Now I would like to talk about Study for jet triger for PbPb 5.5GTeV with ALICE EMCAL,
My name is masato sano.

## Slide 2: Outline
Motivation
ALICE Detector
Annual jet yield with ALICE : PbPb 5.5TeV
ALICE trigger architecture
Jet trigger performance : PbPb 5.5TeV
Summary
Notes: This is outline of this talk.
First I will discuss about motivation for this study.
Then I will show you ALICE detector and Annual jet yield with ALICE
Then I explain the trigger architecture briefly, and then I will show you the jet trigger performance for PbPb 5.5.TeV.
Finally I will summarize this talk.

## Slide 3: Motivation
RHIC has discovered partonic energy loss in QGP
  These results are from the measurement of leading hadrons
If jets can be measured in heavy ion environment, it must be more direct probe for parton energy loss and QGP property itself
Phys.Rev.Lett.91(2003) 072304
Notes: As most of you already know, RHIC has discovered partonic energy loss in QGP,
  Via Significant suppression for high pT hadron and modification on jet like multi-hadron azimuthal correlation.
  These results are mainly from the measurement of leading hadrons.
  If jet can be measured in HI environment, it must be more direct probe for parton energy loss in QGP and QGP property itself.

## Slide 4: ALICE Detector
ITS, TPC, TRD :
  Δφ<2π、|η|<0.9
  charged particle momentum determination.
  Δp/p 〜 5% at 100GeV/c
EMCAL :
  Δφ<110°、|η|<0.7
  π0 and γ measurement
  ΔE/E 〜 11%/√E
Notes: This is ALICE detector which allow us to measure jets even in HI environment.
As you see, there are lots of subsystems in ALICE detector. However, I will introduce part of them which are mainly used for jet measurement.
ITS, TPC and TRD allow us to determin charged particle momentum. Its resolution is about 5% at 100GeV/c.
We have electro magnetic calorimeter. Acceptance is specified here. The energy resolution is here.

## Slide 5: Annual jet yield at ALICE
Annual jet yield
  Nominal PbPb luminosity
  1 running year
  Binary scaling from p+p (pythia6)
  FastJet, anti-kt algorithm is applied for jet reconstruction.
     see next talk by D. Sakata
Huge cross section for jet production!
  200k jets/year above100GeV
  We have lots of opportunity to use jets as a probe for the properties of QGP
ALICE can’t record all events
 Need to trigger
200k
Notes: With This emcal acc., annual yield for inclusive jet is calculated. Horizontal axis is Et cut for jet and vertical axis is annual yield for jet which et is above et cut.
This yield is obtained with nominal PbPb luminosity for 2month and binary scaling from pp.
And jet is reconstructed with fast jet anti kt algorithm.
Different line show different cone size for jet reconstruction.
You can see huge cross section for jet production. So we have lots of opportunity to use jets as a probe for the property of QGP with ALICE

## Slide 6: ALICE trigger architecture
Limitations on data flow
  TPC gating frequency (500Hz)
  High level trigger input bandwidth (25GB/sec)
  Data taping bandwidth (1.25GB/sec)
We have to select the interesting event efficiently
  trigger levels in ALICE (L0(1.2μs), L1(6.6μs), L2 and High level trigger)
For heavy ion jet measurement with EMCAL, the trigger decision is at L1 and High level trigger
L1
Subsystem information only
High Level Trigger
Fully reconstructed event
PbPb L0 frequency : 4kHz
Data rate : 80GB/sec
L1 output should be …
< 500Hz (TPC gating frequency)
< 25GB/sec (High level trigger input bandwidth)
High level trigger output should be …
< 1.25GB/sec (Data taping bandwidth)
Notes:   (However) there are limitations on data flow, TPC gating frequency, High level trigger input bandwidth, Data taping bandwidth.
  Deu to these limitations, we cannot store all data, therefore we have to select the interesting event efficiently.
  For this purpose, we have some levels of trigger in ALICE from L0 to HLT.
  For jet measurement with EMCAL, the trigger is assigned to L1 and High level trigger.
  This schematic view briefly show the data flow related with jet trigger.
  Now We have 4kHz event frequency for PbPb.
  First we select the event in L1 which can use subsystem information only.
  And this L1 output should be less than TPC gating frequency which is 500Hz, and High level trigger input bandwidth of 25GB/sec.
  After that we select the event in HLT which can use fully reconstructed event information.
  This HLT output should be less than Data taping bandwidth which is 1.25GB/sec.
  In this way, we can efficiently select interesting event.
  So how about the trigger performance???

## Slide 7: Jet trigger enhancement with EMCAL
Trigger gain :
  Comparison between
    Jets triggered by and reconstructed with EMCAL
    and
    Jets by geometrical triggers and reconstructed with TPC
  Applicable for ETJet>100GeV
Jet trigger with EMCAL will enhance high pt jet yield
Notes: Assumption luminosity, effective running time, live-time, event rate limitations dut to DAQ bandwidth,

## Slide 8: Study of jet trigger performance : PbPb 5.5 TeV
To evaluate the jet trigger performance in PbPb collision with ALICE EMCAL, I analyzed the PYTHIA events merged with HIJING events, and applied the L1 trigger and High level trigger.
L1 trigger
  Patch trigger algorithm is used with subsystem information only (EMCAL, V0)
    Search the square patch which have maximum amplitude in EMCAL acc.
    If the amplitude is above the threshold, we accept the event
High level trigger
  Fully reconstructed event information (tracks, clusters in EMCAL, …, etc)
  Fastjet Anti-kt algorithm (R=0.4)
    Search the jet which have maximum pT inside EMCAL acc.
    If the pT is above the threshold, we accept the event
EMCAL
Notes: To evaluate the jet trigger performance in PbPb collision with ALICE EMCAL, I analyzed the pythia events merged with Hijing events, and applied the L1 trigger and High level trigger.
For L1 trigger I used partch trigger algorithm with subsystem information only.
Frist I search the square patch which have maximum amplitude in the event.
    And then, If the amplitude is above the threshold, we accept the event.
    For High level trigger I used Fastjet Anti-kt algorithm (R=0.4) is used with fully reconstructed event information.
    First Search the jet which have maximum pT inside EMCAL acc. in the event
    And then, If the pT is above the threshold, we accept the event.

## Slide 9: Background rejection : PbPb 5.5TeV
Left plot :
  Maximum patch amplitude distribution weighted by data volume
  Background only (HIJING)
  Applied cut to reduce data volume by factor 10
Right plot :
  L1 rejection vs L1 output frequency
  Rejection 10  L1 output 110Hz, 8GB/sec
110Hz
Notes: To find threshold which have a certain rejection, I used the number of charged tracks as an event size, which have 75% of a whole size in central PbPb collisions.
I applied the cut to get 10% of total MB data size.

## Slide 10: Trigger bias on jet yield : PbPb 5.5TeV
Upper plot :
  Jet yield as a function of jet pT for pythia before/after trigger
Bottom plot :
  Jet trigger efficiency
Rejections are 10 and 40 for L1 trigger and High level trigger respectively
  L1 output : 110Hz , 8GB/sec
  HLT output : 0.2GB/sec
We have 90 % efficiency at above 80GeV/c for these rejections
90%
Notes: Now this is modification on the jet yield as a funtion of jet pt.

## Slide 11: Summary
Jet Trigger performance was evaluated for PbPb 5.5TeV
Jet trigger efficiency is greater than 90% above 80GeV/c
with the following rejections
  These output are satisfied with the requirements
  (TPC gating frequency, High level trigger input bandwidth and data taping bandwidth)
Centrality dependence of jet trigger performance
Jet trigger performance with the jet quenching model
Jet trigger performance for pp
Outlook
  L1 output : 8GB/sec, 110Hz
  HLT output : 0.2GB/sec
  L1 : 1/10
  HLT : 1/40

## Slide 12: Back up

## Slide 13: ALICE Detector
ITS, TPC, TRD :
  Δφ<2π、|η|<0.9
  charged particle momentum determination.
  Δp/p 〜 5% at 100GeV/c
EMCAL :
  Δφ<110°、|η|<0.7
  π0 and γ measurement
  ΔE/E 〜 11%/√E
JCAL :
  Upgrade of electro magnetic calorimeter in ALICE
  Sitting on back to back side of existent EMCAL in azimuthal angle
  Δφ< 60°,Δη<1.4
  Dijet, pi0-jet, gamma-jet correlation measurement.

## Slide 14: Annual jet yield at ALICE
Annual yield for various jets are calculated.
    Inclusive jet with R=0.4 in EMCAL
    Inclusive jet with R=0.2 in EMCAL
    Jet1 (in Jcal) – jet2(in EMCAL)
    π０ (in Jcal) – jet (in EMCAL)
    γ (in Jcal) – jet (in EMCAL)
  Nominal PbPb luminosity for 2 months.
  Binary scaling from p+p (pythia6)
  FastJet, anti-kt algorithm is applied for jet reconstruction.
We have lots of opportunity to use jets as a probe for the property of QGP !!
Y.Miake, P.Jacobs, H.Yokoyama, M.Sano,

## Slide 15: L1 rejection vs Threshold for PbPb

## Slide 16: Response of the L1 & HLT
Left plot : for L1
  Correlation between “ jet pT in pythia(X axis)” and “amplitude of MaxPatch for L1 in pythia+Hijing(Y axis)”.
  For L1 we can use only partial information like EMCAL cell, V0 and etc. therefore broad correlation can be seen.
Right plot : for HLT
  Correlation between “jet pT in pythia(X axis)” and “pT of Maximum Jet for HLT in pythia+Hijing(Y axis)”.
  For HLT we can use the fully reconstruced information, so much sharper correlation can be seen than L1.
Notes: もっと定量的に見られる図。例えば、50GeV/cのジェットが入った時のresponse.

## Slide 17: Patch size : 0.1x0.1

## Slide 18: Patch size : 0.2x0.2

## Slide 19: Patch size : 0.3x0.3

## Slide 20: Patch size : 0.4x0.4

## Slide 22: Jet trigger efficiency : pp 5.5TeV

## Slide 23: V0 hits vs EMCAL total energy : Background subtraction

## Slide 24: Jet energy resolution
ALICE –EMCAL technical design report