## Slide 1: Memo for the T0/PCR/NTC cable length (for HV and signal)
*** Contents ***
1) Dimensions in IR.
2) Why we need precise length for signal cable?
3) Signal timing chart for T0/PCR.
4) Time variation due to collision points (for HI run, but not pp run).
(Note:) Numbers and contents in
this memo have been updated according
to the “Sep/27, T0/PCR/NTC” meeting

## Slide 2: Dimensions in IR(Signal in blue, HV in yellow) (out of scale drawing)
S
N
Patch panel(need to make)
( 16”W12”D4”H, or
12”W6”D  no-limint_inH )
Nosecone
gap
Width
Depth
Height
(FEM)
Several holes
(need to make)
BBC
T0/PCR/
NTC/ZDC
(clock fanout)
(clock fanout)
NIM
HV
LV power
bucket
(FEM)
LV power
bucket
One existing
4” hole
L(signal B ):
412cm
(162 ”)
L(Signal D):
214cm
(84 ”)
L(Signal C):
(“buffer [ns]” [See next page]
If 20ns, then 400 cm, i.e. 158 ”)
E
W
(North-South orientation is
** INVERSED(!) **
from the Sep/27presentation)
L(signal A, ):
169cm (66 ”)
L(HV (A) ):
169cm(66 ”)
L( HV (B) ):
731cm(288”)
“16 for T0 + 2 for PCR + 8 for NTC + 6spare” sets of
Signal (3 length: A+B(RG8,BNC-BNC), C(RG58BNC-BNC), D(RG58BNC-lemo)),
and HV (1 length (9m): A+B) is needed.
--Rack--
height:
140cm(55”)
width:
61cm(24”)

## Slide 3: Why we need precise signal cable length, How to do ? Constraint due to 1 GTM ( Clock is common for BBC, T0, PCR, NTC, and TOF )
Signal
Clock
~44.75 [ns]
~20[ns]
BECAUSE
~20 [ns]
Signal
Clock
~ 52.9 (T0) +”buffer” [ns]
~ 60.9 (PCR)+”buffer” [ns]
~ (“65to90” + “110”) [ns]
Clock
“a constant time for clock generation”
+ 73.25 [ns]
“a constant time for clock generation”
+73.25 [ns]
+ (60.9 - 44.75) [ns]
+ “buffer” [ns]
“-5.9” to “+10.6” [ns]
“a constant time for clock generation”
+ca.262 [ns]
~ 46 [ns]
Signal
BBC
T0,PCR
TOF
By following method:
(1) The “buffer” [ ns ]
is first set to, let’s say,
20ns(4m).
(2) Then the “buffer” [ ns ]
for T0/PCR
must be swapped with
fine-tuned length
after real pp collision
is measured, (in order
to fit with in the
FEM’s dynamic range(~20ns)).
collision

## Slide 4
Ts_BBC = 44.75ns
Ts_BBC(A)=5.0ns  charged particle flight time (for beta=1; 3.33ns/m, 1.5m)
Ts_BBC(B)=6ns PMT's transit time
Ts_BBC(C)=33.75ns cable (RG58 with75cm of 5ns/m,
Andrew with 675cm of 4ns/m, and RG58 with 65cm of 5ns/m)
Ts_T0(A)=1.8ns [- 0.0ns + 4.7ns]  charged particle flight time
[ nominal value for beta=1; 3.33ns/m, 0.54m]
[ variation is: - 0.0ns, and
+4.7ns for 0.6GeV/c or +3.6ns for 0.7GeV/c or , of Deuteron]
Ts_T0(B) =3.1ns [ + - 3.1 ns ]  light velocity up tp PMT cathode
{Ts_PCR(B) =11.1ns [ + - 3.1 ns ]  light velocity up tp PMT cathode}
[ nominal value for 0.5mScintillator 3.1ns/m(80ps/1.3cm))
[ variation is: ±3.1ns, namely, ±0.5mScintillator]
Ts_T0(C)=9.5ns [ + - 0.44 ns + - 0.15ns] PMT
[nominal value for PMT's Transit Time]
[ variation is: ±0.44ns of TTS, ±0.15ns of PMT variations
±0.15ns of pigtail cable variations]
Ts_T0(D)=43.2ns [ + - 0.13ns ]  cable length
[ nominal value for 7.7ns by Pigtail cable with 154cm of 5ns/s,
24.8ns by RG8 with 581cm of 4.27ns/m
and 10.7ns by LEMO with 214cm of 5ns/m,]
[variation is: the variation of pigtail cable length]
Ts_T0(E)=0.0ns [ + - 2.1ns] collision point
[ variation is: ±2.1ns(3) for Z±63cm ]
Ts_T0{PCR}
=52.9ns{60.9ns}
[-5.9ns,+10.6ns]
Note: Dynamic
range is ~20 [ns]
,where
Ts_T0 =
+Ts_T0(A)
+Ts_T0(B)
+Ts_T0(C)
+Ts_T0(D)
+Ts_T0(E)
,where Ts_BBC =
+Ts_BBC(A)
+Ts_BBC(B)
+Ts_BBC(C)
Signal Timing Chart for T0/PCR. (pp collision is assumed to the time zero.)
See next page
,where
Ts_PCR =
+Ts_T0(A)
+Ts_PCR(B)
+Ts_T0(C)
+Ts_T0(D)
+Ts_T0(E)

## Slide 5: Time variation due to collision points. (for Y2001-HI run, [but not pp run]) from online logbook (the plot was shown at RHIC time meeting)
PHENIX RUN LOG
Tue Sep 18 02:49:16 2001
by T.Hachiya
Run 28282.
This was the first RUN after
200MHz RF was used with
56 bunchs. Plots are timing
distributions of each side
of BBBBC.
ZDC scale down factor was
already corrected. It is expected
to be BBC Z-vertex distribution
triggered by inclusive ZDCNS.
South
Difference
North
 | Height (a.u.) | Mean (cm) | Sigma (cm)
Beam gas | p0 | p1 | p2
Au Au Collision | p3 | p4 | p5 = 20.85cm
Beam gas | p6 | p7 | p8
3 gaussian fit
y=
+p0 * exp ( -0.5 * {(x - p1) / p2} 2 )
+p3 * exp ( -0.5 * {(x - p4) / p5} 2 )
+p6 * exp ( -0.5 * {(x - p7) / p8} 2 )
Au+Au
Beam gas
Beam gas
Within ±1(i.e.±0.695ns) : 68.3%
Within ±2(i.e.±1.390ns) : 95.5%
Within ±3(i.e.±2.085ns) : 99.7%
Within ±4(i.e.±2.780ns) : 99.99%